## Slide 2: -EEW-
Calculation of an Earthquake’s Magnitude From The First Three Seconds of its P Wave Amplitude
By – Jabir Rahman

## Slide 3: Types and Use
Regional Warning
Uses traditional methods
Locating, measuring, warning
On Site Warning -
Real time warning
Doesn’t necessarily need precise Magnitude or Location
Taiwan, Japan, Mexico etc.

## Slide 4: Pros and Cons
Regional Warning
Reliable
Slow
On Site Warning
Quick
Not so precise

## Slide 5: What Do We Want With On Site Warning!
IRAN-IRAQ BORDER
MEXICO

## Slide 6: Why P?
Reaches First
Less Destructive
Travels in All Medium

## Slide 7: Steps in My Project
Collecting Data
Processing Data
Calculation

## Slide 8: First Step
Mexico and Gulf of Mexico
First Seven Months of This Year
-Magnitude >=4
-Single Station Method

## Slide 9: Second Step
Focal Mechanism

## Slide 10: Equation Derivation
Use Matlab to Calculate Maximum Displacement and Maximum Velocity within 3 seconds of P arrival
M_calculated = (4.5 + (1.37*log(dis_max)) + (1.88*log((distance)/111)) - (log(vel_max)))

## Slide 11: Results and Conclusion
Chart: 
M Actual | 4.8 | 4.8 | 4.6 | 4.6 | 4.9 | 4.9 | 4.7 | 4.7 | 4.7 | 4.7 | 4.5 | 4.5 | 4.3 | 4.3 | 4 | 4 | 4 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3
M Calculated | 4.7627 | 4.7314 | 9.7037 | 9.7328 | 10.6549 | 9.9548 | 4.1889 | 4.1793 | 9.2008 | 8.6275 | 10.012 | 9.4704 | 4.6442 | 5.1452 | 9.8769 | 9.5326 | 10.1011 | 10.2477 | 5.559 | 7.7794 | 7.8031 | 9.7629 | 9.1258 | 7.9477 | 5.544 | 7.7495 | 8.886 | 8.2797

## Slide 12: Comments
Most values cam bigger than the actual values (Negative)
Did not miss even a single one
Better to live than to be precise !!!!

## Slide 13
Thank You!